## Slide 1
SMART INDIA HACKATHON 2026
SatQuery AI
Natural language in. Validated remote-sensing workflows out.
An agentic reasoning and orchestration layer that turns a geospatial question into a decomposed, capability-matched, deterministically validated remote-sensing workflow — and returns an interpretable answer with its evidence.
Natural-language intent
Reason · decompose · plan
Deterministic validation
Specialist RS execution
Evidence-backed answer
PROBLEM STATEMENT ID
SIH26167
PROBLEM STATEMENT TITLE
[ FILL FROM SIH PORTAL ]
THEME
[ FILL ]
PS CATEGORY
Software
TEAM ID
[ FILL ]
TEAM NAME
[ FILL ]
Notes: We are presenting SatQuery AI for problem statement SIH26167. In one line: SatQuery turns a plain-language geospatial question into a validated, executable remote-sensing workflow. The important word is validated. Through this deck we will show you exactly where AI reasoning stops and deterministic engineering takes over, because that boundary is the core of our design.

## Slide 2
Proposed Solution
SIH 2026 · SatQuery AI · PS SIH26167
2
The model decides WHAT should happen. Deterministic code verifies WHETHER it can safely happen.
ONE QUESTION, END TO END
“Identify areas where vegetation decreased significantly between 2023 and 2025.”
1 UNDERSTAND
intent, entities, region, 2023 ↔ 2025
2 DECOMPOSE
7 subtasks planned for this question
3 INFER INPUTS
optical · RED+NIR 2 dated scenes · CRS
4 SELECT
change_detection (index = NDVI)
5 VALIDATE
bands ✓ count ✓ CRS ✓ dates ✓
6 EXECUTE
NDVI ×2 → align → Δ → σ-threshold
7 INTEGRATE
evidence → map, stats, explanation
Output: loss percentage · spatial hotspot map · per-region statistics · plain-language explanation · full provenance of every step
INNOVATION AND UNIQUENESS
Reasoning ≠ verification
The model proposes a workflow; the registry and validator decide whether it may run. A reasoning error becomes a precise rejection, never a confident wrong map.
Capability-aware selection
Tools are matched against declared contracts — modality, required bands, image count, temporal pairing — not by keyword similarity.
Composable operations
A single question can chain index computation, co-registration, differencing, thresholding and spatial aggregation into one workflow.
Extensible by declaration
A new model joins by adding a registry entry and a binding. The controller, validator and API stay unchanged.
Notes: Take this question. A person asks it in one sentence, but answering it requires spatial reasoning, temporal reasoning, band selection, index computation, co-registration, differencing and statistical thresholding. SatQuery derives all seven stages from the sentence. Look closely at stages four and five. A capability is chosen from a registry, and only then does deterministic code check whether the imagery can actually support it. The model proposes; the system verifies.

## Slide 3
Technical Approach
SIH 2026 · SatQuery AI · PS SIH26167
3
AI reasoning proposes → deterministic layers verify, execute and explain
AI reasoning
Deterministic
Live today
Planned
INTERFACE
what the user gives
Natural-language question + satellite imagery (GeoTIFF / Sentinel-2 / Landsat) + optional region and dates
REASONING
LLM proposes
Query understanding
intent · entities · spatial + temporal constraints
Task decomposition
one question → ordered executable subtasks
Input requirement inference
modality · bands · image count · metadata
CAPABILITY REGISTRY
the contract
8 versioned capabilities
the only functions the agent may call
tool_id · description · supported modalities · required bands · min/max images · temporal-pair flag · parameter schema
constrains capability selection AND supplies the constraints the validation gate enforces
ORCHESTRATION
planning the run
Capability selection
match subtask against registry contracts
Execution planning
order, dependencies, intermediate artefacts
Parameter configuration
bands, scale/offset, thresholds, masking
VALIDATION GATE
hard boundary
DETERMINISTIC INPUT AND COMPATIBILITY VALIDATION
image count · metadata present · modality · temporal information · CRS · required spectral bands (cross-vocabulary: B4 ≡ red) · optical / SAR · temporal-pair distinctness
No LLM opinion can bypass this. Nothing executes until it passes.
✓ proceed
✗ reject
with the exact reason
REMOTE-SENSING EXECUTION
specialist compute
NDVI
NDWI
NDBI
Bi-temporal change detection
Satellite VQA
Land-cover classification
Object detection
SAR analysis
EVIDENCE & RESULT
making it an answer
Heterogeneous outputs
raster · mask · bounding boxes · classes · statistics · temporal delta · confidence
Aggregated → spatially and temporally interpreted → human-readable answer + map + statistics + provenance
RE-PLAN on failure, rejection or low confidence
Notes: This is the architecture. Orange is where the language model reasons: understanding, decomposition, requirement inference. Everything below it is deterministic. The registry is the only door — the agent cannot call a function that is not declared there, and those same declarations supply the constraints the validation gate enforces. The gate is a hard boundary; no model opinion crosses it. Execution is a separate specialist layer. And when a run is rejected or returns low confidence, the system re-plans rather than failing silently.

## Slide 4
Feasibility and Viability
SIH 2026 · SatQuery AI · PS SIH26167
4
ALREADY BUILT AND PROVEN
326
automated tests passing
8
capabilities in the registry
4
specialist tools executing today
2
interchangeable raster backends
VALIDATED
Ten-stage controller pipeline
understanding → classification → planning → requirements → selection → validation → configuration → execution → integration
VALIDATED
Deterministic validator — 8 check families
count, metadata, modality, temporal, CRS, bands, optical/SAR, pair distinctness
VALIDATED
Capability registry + implementation binding
an implementation can never expose a capability the registry has not sanctioned
VALIDATED
NDVI, NDWI, NDBI on real rasters
sensor scale/offset handling, SCL / QA_PIXEL cloud and shadow masking
VALIDATED
Bi-temporal change detection
co-registration guard, Δ-index arithmetic, σ-based significance thresholding
VALIDATED
Dual raster backend
rasterio/GDAL, plus a dependency-free GeoTIFF codec; tests prove both agree
VALIDATED
HTTP service — 8 endpoints
submit, validate-only, list, fetch, artefact download, registry, health
INTEGRATING
LLM reasoning and decomposition layer
the pipeline is already shaped to receive it; registry + validator keep the veto
NEXT STAGE
VQA, land-cover, detection, SAR specialists
declared in the registry today; the executor reports them honestly as unbound
RISKS AND HOW WE CONTAIN THEM
Reasoning proposes an invalid workflow
The registry bounds what can be called and the validator bounds what can run. A bad plan is refused with a reason, not executed.
Heavy GDAL dependency blocks deployment
A dependency-free GeoTIFF path ships alongside rasterio, and the test suite proves the two backends produce identical results.
A misaligned image pair yields a confident, wrong change map
Alignment is checked on grid, CRS, pixel size and origin before any arithmetic — and refuses rather than silently resampling.
Cloud contamination distorts index statistics
Sentinel-2 SCL and Landsat QA_PIXEL masking, plus baseline 04.00 scale/offset correction, are applied before aggregation.
New models force a core rewrite
Adding a capability is a registry entry plus a binding. The controller, validator and API are untouched.
Notes: This is what already runs, not what we intend to build. Three hundred and twenty-six automated tests pass. Eight capabilities are declared and four execute on real rasters today, including bi-temporal change detection. We ship two interchangeable raster backends and the tests prove they agree, so a GDAL-free deployment is possible. We are explicit about status: the reasoning layer is being integrated, and four specialists are declared but not yet bound. On risk — our containment is not a promise that the model behaves. It is that the registry and the validator hold the veto regardless of what the model proposes.

## Slide 5
Impact and Benefits
SIH 2026 · SatQuery AI · PS SIH26167
5
THE CHANGE SATQUERY MAKES
TODAY
Raw satellite data
Domain expert required
Manual preprocessing
Manual tool selection
Isolated algorithms
Fragmented, unexplained results
SATQUERY
Natural-language intent
Task reasoning
Workflow decomposition
Capability selection
Deterministic validation
Specialist RS execution
Evidence integration
Interpretable geospatial answer
WHO THIS REACHES
Agriculture departments
crop stress, sowing extent and seasonal vegetation loss without a GIS analyst in the loop
Disaster response
rapid before/after assessment of flood, fire and landslide extent from a plain question
Urban planning bodies
built-up growth and encroachment measured over time with a reproducible method
Forest and environment
deforestation and water-body change tracked with auditable, repeatable evidence
Space and defence analysts
a controlled, extensible surface for adding new specialist models safely
Students and researchers
remote-sensing analysis becomes accessible without mastering the toolchain first
BENEFITS
Social
Geospatial evidence stops being the preserve of trained specialists. A district officer can ask a question in their own words and receive a defensible, explained answer.
Economic
Removes repeated manual preprocessing and per-task scripting. One controlled workflow layer serves many departments instead of each rebuilding its own analysis chain.
Environmental
Makes routine monitoring of vegetation loss, water extent and built-up encroachment cheap enough to run often — which is what turns monitoring into intervention.
Operational
Every answer carries its provenance: which tool ran, on which imagery, with which parameters. Results are reproducible and auditable, not one-off outputs.
Notes: Today, answering a geospatial question needs an expert, manual preprocessing and manual tool selection, and the results arrive fragmented. SatQuery collapses that into a question. That matters most where expertise is scarce — a district agriculture office, or a disaster cell in the first hours of a flood. And because every answer carries its provenance, the output is auditable and reproducible rather than a one-off image someone produced once.

## Slide 6
Research and References
SIH 2026 · SatQuery AI · PS SIH26167
6
WHY THE ARCHITECTURE IS SHAPED THIS WAY
Agentic planning and task decomposition
Interleaved reasoning and acting lets one question become an ordered set of executable subtasks instead of a single opaque call.
→ Reasoning layer
Schema-constrained tool calling
A model calling arbitrary functions is unsafe on real data. Calls are restricted to declared signatures with typed parameters.
→ Capability registry
Capability-aware orchestration
Selection is driven by each tool's declared input contract — modality, bands, image count — not by name similarity to the query.
→ Selection stage
Deterministic verification of model output
Language models are strong proposers and unreliable verifiers, so technical admissibility is decided by code that cannot be persuaded.
→ Validation gate
Remote-sensing foundation models and VQA
Pretrained geospatial and multimodal models supply scene-level understanding that index arithmetic alone cannot express.
→ Execution layer (next stage)
Multi-temporal analysis and provenance
Change is only meaningful on co-registered pairs, and an answer is only trustworthy when the path that produced it is recorded.
→ Execution + evidence integration
REFERENCES
• Yao et al., ReAct: Synergizing Reasoning and Acting in Language Models, ICLR 2023.
• Schick et al., Toolformer: Language Models Can Teach Themselves to Use Tools, NeurIPS 2023.
• Patil et al., Gorilla: Large Language Model Connected with Massive APIs, 2023.
• Jakubik et al., Foundation Models for Generalist Geospatial Artificial Intelligence (Prithvi, IBM–NASA), 2023.
• Lobry et al., RSVQA: Visual Question Answering for Remote Sensing Data, IEEE TGRS 2020.
• Bastani et al., SatlasPretrain: A Large-Scale Dataset for Remote Sensing Image Understanding, ICCV 2023.
• ESA, Sentinel-2 Level-2A Product Specification — Scene Classification (SCL) and processing baseline 04.00 offsets.
• USGS, Landsat Collection 2 Level-2 Science Products — QA_PIXEL bit definitions.
Implementation: github.com/VinayakGupta-1/SatQuery-AI · Live demo: [ INSERT WEB DEMO LINK ]
Notes: Each design choice traces to a body of work rather than to a trend. Agentic planning gives us decomposition. Schema-constrained tool calling is why we built a registry instead of allowing free-form function access. The most important is the fourth: language models are strong proposers and unreliable verifiers. That finding is precisely why our validation gate is code, and not a prompt.

## Slide 7
Appendix — Capability contracts and the validation gate
SIH 2026 · SatQuery AI · PS SIH26167
7
A REGISTRY ENTRY IS A CONTRACT
change_detection
name
Bi-Temporal Change Detection
tool_type
change_detection
supported_modalities
optical, SAR
min / max images
2 / 2
requires_temporal_pair
true
parameters
index, band overrides, threshold, threshold_method, sigma_multiplier, scale, offset, mask_band, sensor
enabled
true
The agent may call this and nothing else. Capability selection and the validation gate both read from here.
THE GATE, IN PRACTICE
✓
Two images supplied?
count checked against min/max from the registry
✓
Both optical?
modality read from metadata, compared to the contract
✓
RED and NIR present?
band names canonicalised first, so B4 ≡ red ≡ B04
✓
Acquisition dates present and different?
a “change” between one date and itself is refused
✓
Same CRS, grid, pixel size and origin?
checked before arithmetic — refuses, never silently resamples
When a check fails
The run stops before execution and returns the failing check, the field it applies to and a machine-readable error code — so the user is told what to fix, and a re-plan has something concrete to act on.
Declared ≠ implemented
Four of the eight registered capabilities have real implementations bound today. The other four are declared contracts with no binding — and the executor reports exactly that instead of returning a placeholder result. Being honest about what actually runs is part of the design, not a gap in it.
Notes: If you want the mechanism: this is a real registry entry. It declares modality, band requirements, image count, temporal pairing and a parameter schema. Selection reads it and the validator reads it. On the right are the five checks that run before a single pixel is touched. Note the last one — a misaligned pair would produce a confident and completely wrong change map, so we refuse rather than silently resampling the user’s imagery. And we state plainly that four capabilities are declared without implementations.

## Slide 8
Appendix — Interface, demo and code
SIH 2026 · SatQuery AI · PS SIH26167
8
WEB INTERFACE
[ INSERT WEB INTERFACE SCREENSHOT ]
query box · uploaded scenes · validation verdict · workflow trace · result map and statistics
SAMPLE OUTPUTS
[ NDVI RASTER OUTPUT ]
[ CHANGE HOTSPOT MAP ]
CODE AND DEMO
[ QR ]
GITHUB
github.com/VinayakGupta-1/ SatQuery-AI
LIVE DEMO
[ INSERT WEB DEMO LINK ]
Notes: This is the web interface and the repository. We are happy to run a live query on real imagery now if you would like to see the full trace.

## Slide 9
Appendix — Scaling beyond the current implementation
SIH 2026 · SatQuery AI · PS SIH26167
9
WHAT GROWS, STAGE BY STAGE
NOW
Deterministic core
Ten-stage pipeline, registry, validator and four executing remote-sensing tools, covered by 326 passing tests.
INTEGRATING
Reasoning layer
An LLM proposes the interpretation, decomposition and parameters. The registry and validator keep their veto over everything it proposes.
NEXT
Specialist model tier
VQA, land-cover classification, object detection and SAR analysis bind to contracts that already exist in the registry.
THEN
Data and scale tier
Catalogue-backed imagery search, tiled and distributed execution, cached intermediate artefacts, multi-step composed workflows.
WHAT DOES NOT CHANGE AS IT GROWS
The validation gate stays in the path
Every new capability is validated against its own declared contract by the same deterministic code. Adding models never widens the trust boundary.
The registry stays the only door
A capability that is not declared cannot be selected and cannot be executed, however the reasoning layer is prompted.
The controller stays untouched
Extending the system is a registry entry plus a bound implementation. No orchestration rewrite, no API change.
SatQuery AI is not a chatbot over satellite imagery. It is a reasoning and orchestration layer that turns natural-language geospatial intent into validated, executable remote-sensing workflows.
Notes: On scale: the reasoning tier is being integrated now, the specialist models bind to contracts that already exist in the registry, and the data tier follows. The point of this slide is the bottom row. None of that growth widens the trust boundary. Every new capability is validated by the same deterministic code against its own declared contract. Extending SatQuery is a registry entry and a binding — never a rewrite.